Tornado 5.5m – “Crawley Divers”

| Marine VHF Radio | On top of console. Requires Electrical Isolator to be on. Requires Radio/Nav Switch to be on. |
| --- | --- |
| Oxygen Administration Kit | Marinox Oxygen Set on Bottle Rack |
| First Aid Kit | In White Tub on top of “A” frame |
| Distress Flares | In Yellow Container on Port Side |
| Engine Spares and Tools | In Yellow Container on Starboard Side |
| Anchor and Anchor Line | In Bow Locker, attached to underside of cleat. |
| Bellows | In Bow Locker |
| Oars | Inside rear tubes to port and starboard |
| Fire Extinguisher | In Grey Tube on Bottle Rack |
| Spare Fuel | In Red Container at rear of boat. Plugs into engine fuel adapter. Unmixed. |
| Spare Oil | In Yellow Container on Port Side |
| Bilge Pump | On floor at rear. Requires Electrical Isolator to be on. Requires Aux Switch to be on. |
| Mooring Lines | Painter on bow, port and starboard stern lines. |
| Fuel filler | On front of console. 100L tank. Unleaded Fuel. |
| Oil filler | Inside engine cowling. Access via front plate. |
| Engine Controls | On left of console. Key (push for choke) Kill Switch and Cord Tilt switch on inside of throttle lever |
| Battery | On box on floor in front of console |
| Fuel Filter | On inside of transom |
| “A” Flag | At rear of boat on Port Side. Inserts into tube on Port Side of “A” frame. |

Notes on Operation

The engine will be difficult to start unless it is fully tilted down and the fuel bulb properly primed.

If engine is cold, advance the fast idle speed lever  or throttle only feature to an approximate halfway (1/2) setting. After engine start up, immediately adjust neutral fast idle setting so engine speed drops below 2000 RPM. Return back to normal idle speed after engine is warmed up.

Turn ignition key to START position and start the engine. If engine is cold, push in on key to prime the engine while cranking. If engine fails to start in ten seconds, wait 30 seconds and try again. If engine begins to stall, re-prime (push key in) until engine is running smoothly.

Warning System

1 The outboard warning system incorporates a warning horn inside the boat.

The warning horn on remote control operated models may be located inside the remote control or connected to the key switch under the dash. On tiller handle models the warning horn is located below the tiller handle.

The warning horn will emit a continuous beep. This will alert the operator to one of two problems: EITHER an engine overheat condition OR low oil level in the oil injection tank. See explanations “2” and “3” following.

2 Engine overheat

If the engine overheats, the warning horn will sound. Immediately reduce throttle speed to idle. Shift outboard into neutral and check for a steady stream of water coming out of the water pump indicator hole. If no water is coming out of the water pump indicator hole or flow is intermittent,

stop engine and check water intake for obstruction. If no obstruction is found, this may indicate a blockage in the cooling system or a water pump problem. Have the outboard checked by your dealer. Operating the engine while overheated will cause engine damage.

If a steady stream of water is coming out of the water pump indicator hole, and the warning horn continues to sound, there still may be insufficient cooling water or an engine problem. Stop engine and have it checked by your dealer. Operating the engine while overheated will cause engine damage.

Note: Should this occur and you are in a stranded situation, stopping the engine and allowing it to cool back down will usually allow some additional low speed (idle) running time before the engine starts to overheat again. The overheat problem must be corrected before you can resume normal

operation.

3 Low oil level in the oil injection system.

If the oil level drops below the low oil level, the warning horn will sound. You still have an oil reserve remaining for 30 minutes of full speed operation.